## Slide 2
Reliable VPN Solutions IN
IOT Environments
JULIAN WEINBERGER | +1 (650) 316 6273 | www.ncp-e.com

## Slide 3: SECURE COMMUNICATION IN IOT ENVIRONMENTS
GROWTH OF IOT ENVIRONMENTS
IOT MARKET FORECASTS VARY; ALL PREDICT ENORMOUS GROWTH POTENTIAL.
PREDICTIONS FOR 2020 RANGE FROM 12 TO 50 BILLION, UP FROM 1 BILLION IN 2010

## Slide 4: SECURE COMMUNICATION IN IOT ENVIRONMENTS
IMPLEMENTATION APPROACHES FOR VPN AND IOT
VPN provided by a router via WiFi/HotSpot
VPN Software
No additional hardware/services required
Traffic encrypted on the device
VPN provided by a carrier via 3G/4G LTE

## Slide 5: SECURE COMMUNICATION IN IOT ENVIRONMENTS
VPN Connections
Connection type depends on the machine application
Automatic, or always on
  e.g, surveillance camera
Connection on demand, via command line or API
  e.g., credit card swipe at POS terminal
VPN
Management
Gateway

## Slide 6: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Authenticating the connection
In the absence of human interaction, a machine needs to perform authentication steps to establish a VPN connection.
Username / Password
Soft certificates
Smartcards
Hardware / Machine
certificates
TPM

## Slide 7: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Authentication methods at a glance

## Slide 8: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Authentication methods
Username / Password
  Commonly stored in VPN Client on the machine
  Credentials can be information e.g. the hostname
Soft Certificates
  User certificates stored on local device
  Every machine has one certificate, which may not be unique to it

## Slide 9: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Authentication methods
Smartcards
  Physical external smartcard for authentication
  User certificate on external chip
  Adds another level of security
  Basis for two-factor-authentication
Machine hardware certificates
  User/soft certificates relies on machine fingerprint to bind to unique machine
  Can not be used with any other machine
  Basis for two-factor-authentication

## Slide 10: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Authentication methods
TPM (Trusted Platform Module)
  Smartcard build into machine, soldered onto motherboard
  Adds another level of security
  Basis for two-factor-authentication

## Slide 11: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Managing the Vpn Client
Full control, everywhere at any time
Rollout of software, configurations and authentication information
Configuration and software updates
VPN Management
Authentication management
VPN
Management
Gateway

## Slide 12: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Endpoint Policy
Software deployment
VPN Gateway
VPN Central Management - the Single Point of Administration
RADIUS Server
Certification Authority (CA)
USER directory

## Slide 13: SECURE COMMUNICATION IN IOT ENVIRONMENTS
Summary
VPN has been the basis for securing IoT environments for some time
Automatic, always-on vs. connection on demand is based on application type
Consider resources, flexibility and security when selecting authentication method(s)
Look for solutions that enable automatic rollout of VPN configurations, certificates and updates

## Slide 14: Scenario
Fleet Management – Connected Cars
Operational information for 10,000 vehicles
Onboard Unit with
IIoT Remote Gateway
IIoT
Management
IIoT Gateway
NCP Secure
Client
Data Center
lan
Wifi

## Slide 15: Scenario
Tramway-Information system
Information directly on info displays and ticket vending machines
Info display
Ticket Vending Machine
IIoT Remote Gateway
IIoT Remote Gateway
IIoT
Management
IIoT Gateway
Data Center
lan
3G/4G
wifi

## Slide 16: Scenario
Secure IN-Store digital display for product promotion
Service Technician
Content
Grocery store, medical Pracitce, Pharmacy…
Content Management System
IIoT
Management
IIoT Gateway
lan
3G/4G
wifi
Data Center
Digtial signage at grocery stores or pharmacies

## Slide 17: SECURE COMMUNICATION IN IOT ENVIRONMENTS
30 YEARS REMOTE ACCESS – SECURE COMMUNICATION EXPERTISE
headquarters
founded 1986
100 % privately owned
Nuremberg - Germany
About NCP engineering – Network Communication Products
established 2010
Clearwater - Florida
established 2015
San francisco - California
global support team
global network of sales partner
international OEM partnerships
worldwide more than 30,000 customers

## Slide 18
Thank you For your Attention
JULIAN WEINBERGER | +1 (650) 316 6273 | www.ncp-e.com